## Slide 1
SIH26052 · DRDO · HARDWARE THEME · SMART VEHICLES
AEGIS-COM
Event-Aware Adaptive Speech Protection for Defence Communications
▸ Radio commands fail when engine, rotor, and impulsive noise hit the same sentence.
▸ LMS / Wiener / spectral subtraction lag or break on bangs.
▸ We are not showing a fake tactical headset. We show a comms-path controller.
▸ Sense the event → switch enhancement policy → recover the next word.
ONE PIPELINE
Acoustic intelligence
FSM controller
Mode-specific SE
Recover after impulse
Laptop POC = software-in-the-loop digital enhancement. Physical earcup ANC = future companion, not today’s claim.
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 1/6
Notes: Open with lost radio commands. Name DRDO. Say laptop POC immediately. Do not say we built a headset.

## Slide 2
Existing systems already protect hearing. The gap is elsewhere.
MATURE TODAY
▸ 3M ComTac VI: impulse + steady hearing protection (ANSI S12.42).
▸ Mission Audio Profiles: Comfort / Conversation / Patrol / Observation — operator selected.
▸ INVISIO RA108 / RA5100: PNR + ANR for continuous vehicle noise; user-toggled hear-through.
▸ Generic AI denoisers: one policy for every scene.
THE REAL GAP
▸ MAP is a menu, not a closed loop on the radio path.
▸ ANR is built for rumble, not policy switching after a bang.
▸ AI denoisers smear the next syllable when the noise model is poisoned.
▸ Missing: automatic, confidence-gated enhancement policy + mandatory recovery.
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 2/6
Notes: Never say existing headsets cannot handle impulse. Contrast MAP vs automatic comms policy.

## Slide 3
Novelty: event-aware policy switching, not ‘AI + DSP’
AUDIO
SENSE
DECIDE
PROCESS
RECOVER
SPEECH PRESERVE
STATIONARY
DYNAMIC
IMPULSE PROTECT
RECOVERY
▸ Every 16 ms we estimate class, severity, speech P, impulse P, confidence — then the FSM chooses a mode.
▸ Impulse has priority and FREEZES the noise estimate. Recovery is mandatory. Low confidence holds the last stable mode.
▸ AI (RNNoise-class on the edge; Wiener in tonight’s POC) is a module inside STATIONARY/DYNAMIC — not the invention.
▸ This is complementary to ComTac MAP / INVISIO ANR, not a claim that those products lack hearing protection.
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 3/6
Notes: Point to RECOVERY. Invention is the mechanism. Enhancer is swappable.

## Slide 4
Working POC — real processing on a laptop
REAL
Detector, FSM, Wiener, waveforms, spectrograms, SNR, SI-SNR, laptop RTF
SIMULATED
Formant speech, engine/rotor-like noise, laboratory impulse — not field tapes
TARGET
SNR > 15 dB · STOI > 0.85 · PESQ > 2.5 (SIH goals, not claimed)
FUTURE
Jetson / Pi / DSP, dual-mic ANC, tactical headset, DRDO field audio
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 4/6
Notes: START DEMO after this slide if time: clean → engine → dynamic → impulse → recovery.

## Slide 5
Laptop measurements on the synthetic demo scene
Input SNR (dB)
0.22
Output SNR (dB)
2.15
SNR improvement (dB)
1.92
SI-SNR in / out (dB)
5.42 → 8.09
Impulse peak reduction (dB)
11.08
Detect latency / recovery (ms)
0.00 / 416.00
Laptop RTF
0.01
STOI
0.785 (MEASURED)
PESQ
UNAVAILABLE — TARGET 2.5
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 5/6
Notes: Read only these numbers. SIH printed thresholds are TARGETS. Hardware was not used.

## Slide 6
Path to hardware, impact, frozen novelty
▸ Deploy path: laptop SIL → USB audio → Raspberry Pi / Jetson → boom-mic + certified earcup ANR.
▸ Latency budget (ESTIMATE): 16 ms hop + model + I/O < 60 ms. Laptop RTF is the measured number today.
▸ Impact: fewer lost commands when the scene jumps; software updates without replacing every headset.
▸ Novelty recap: automatic event-aware speech-protection policy with impulse freeze and recovery.
POC today
Edge port
Headset I/O
Field trial
We are not asking DRDO to believe a dashboard. We are asking them to believe a controller that changes its mind for a reason — and we showed that reason on audio.
SIH26052 · DRDO · AEGIS-COM · Internal hackathon POC · 6/6
Notes: Close on Indian software on the comms stack, not replacing ComTac. Invite the demo.